## Slide 1
Module 2
IEEE 1364-2001 (Verilog-2001)
learn_verilog_systemverilog / Module 2

## Slide 2
Learning objectives
• Master the major Verilog update (IEEE 1364-2001) and
its additions over 1364-1995: ANSI ports, impl…
learn_verilog_systemverilog / Module 2

## Slide 3
Prerequisites
• See module README
learn_verilog_systemverilog / Module 2

## Slide 4
Learning path
Master the major Verilog update (IEEE 1364-2001) and its additions over 1364-1995: ANSI ports, implicit sensitivity, generate, signed types…
learn_verilog_systemverilog / Module 2

## Slide 5
Overview
• This module covers IEEE Std 1364-2001
(Verilog-2001), the first major revision of the
Verilog stand…
learn_verilog_systemverilog / Module 2

## Slide 6
Syllabus topics
learn_verilog_systemverilog / Module 2

## Slide 7
1. IEEE 1364-2001 Context (1/2)
• ANSI-style port declarations: Direction and type
(and size) in the port list
• **`always @*`**: Implicit sensitivity for
combinational logic (no manual list)
• generate: Conditional and loop-based instantiation
and logic
• signed: Signed arithmetic and signed nets/variables
• Multi-dimensional arrays: e.g. `reg [7:0] mem
[0:255]`
• localparam: Named constants that cannot be
overridden
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 8
1. IEEE 1364-2001 Context (2/2)
• ANSI-style task/function: Input/output in the header
• Other: File I/O improvements, `$signed`/`$unsigned`,
attribute syntax, etc.
• No SystemVerilog: no `logic`,
`always_comb`/`always_ff`, interfaces, packages,
classes
• No type parameters or interfaces (those are 1800)
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 9
2. ANSI-Style Port Declarations (2001)
• input wire: Default for input; can omit `wire` (e.g.
`input [7:0] a`).
• output reg: Required when the output is driven in
`always`/`initial`.
• output wire: When the output is driven only by
`assign` or submodule.
• Same behavior; 2001 is more concise and keeps port
and type in one place.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 10
3. Implicit Sensitivity: always @* (2001)
• **`@*` (or `@(*)`**): Sensitive to every signal read
in the block (RHS and conditions).
• Use for combinational logic only; do not use for
sequential (use `always @(posedge clk)`).
• **Prefer `@*`**: For combinational blocks; fewer
errors, easier to maintain.
• Explicit list: When targeting strict 1995
compatibility or when a tool does not support `@*`.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 11
4. Generate (2001)
• genvar: Loop variable for generate loops; not a
runtime variable.
• generate for: Replicates logic/instances; index must
be constant at elaboration.
• generate if / else: Choose one of several
implementations at elaboration.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 12
5. Signed Types (2001)
• signed: Affects arithmetic and comparison in
expressions involving that net/reg.
• Unsigned (default): No sign extension; values 0 to
2^N-1.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 13
6. Multi-Dimensional Arrays (2001)
• Packed (left): `[7:0]` — contiguous bits, can be
used as a single vector.
• Unpacked (right): `[0:255]` — array of elements;
select with one index at a time in 2001.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 14
7. localparam (2001)
• parameter: Can be overridden: `#(.WIDTH(16))`.
• localparam: Cannot be overridden; often derived from
parameters or fixed.
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 15
8. ANSI-Style Tasks and Functions (2001)
• automatic: Optional; gives automatic storage (re-
entrant). Useful for recursive or concurrent calls.
• input/output in header: Cleaner than 1995 style;
avoids duplicate declarations.
• Note: In 1364-2001 use `output reg` (not `output
logic`; `logic` is SystemVerilog).
learn_verilog_systemverilog / Module 2
Notes: From MODULE2 Topics Covered.

## Slide 16
Hands-on examples
learn_verilog_systemverilog / Module 2

## Slide 17
Module 2 toolchain check
$ command -v iverilog >/dev/null && echo "Toolchain ready: $(iverilog
-V 2>&1 | head -1)"
learn_verilog_systemverilog / Module 2
Notes: Requires iverilog on PATH (apt install iverilog).

## Slide 18
Demo: ANSI Ports
$ cd module2/examples/ansi_ports && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/ansi_ports/

## Slide 19
Demo: always @*
$ cd module2/examples/procedural && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/procedural/

## Slide 20
Demo: Generate
$ cd module2/examples/generate && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/generate/

## Slide 21
Demo: Generate if/else
$ cd module2/examples/generate_if && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/generate_if/

## Slide 22
Demo: Generate Ripple Adder
$ cd module2/examples/generate_ripple_adder && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/generate_ripple_adder/

## Slide 23
Demo: Signed
$ cd module2/examples/signed && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/signed/

## Slide 24
Demo: Signed vs Unsigned Comparison
$ cd module2/examples/signed_compare && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/signed_compare/

## Slide 25
Demo: Decoder
$ cd module2/examples/decoder && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/decoder/

## Slide 26
Demo: Multi-Dimensional Arrays
$ cd module2/examples/arrays && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/arrays/

## Slide 27
Demo: Multi-Dim Style
$ cd module2/examples/multi_dim_arrays && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/multi_dim_arrays/

## Slide 28
Demo: Parameters and localparam
$ cd module2/examples/parameters && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/parameters/

## Slide 29
Demo: ANSI Task/Function
$ cd module2/examples/tasks_functions && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/tasks_functions/

## Slide 30
Demo: ANSI Task with Output
$ cd module2/examples/task_ansi && make clean && make run
learn_verilog_systemverilog / Module 2
Notes: Hands-on: module2/examples/task_ansi/

## Slide 31
Practice & assessment
learn_verilog_systemverilog / Module 2

## Slide 32
Exercises
• ANSI Ports
• always @
• Generate
• Signed
• Arrays and localparam
learn_verilog_systemverilog / Module 2

## Slide 33
Exercises
• Using always @* for Sequential Logic
• genvar in Normal Code
• Overriding localparam
• Signed vs Unsigned Mix
• Generate Block Scope
learn_verilog_systemverilog / Module 2

## Slide 34
Summary & next steps
• Master the major Verilog update (IEEE 1364-2001) and
its additions over 1364-1995: ANSI ports, impl…
• Complete module2/CHECKLIST.md
• Run ./scripts/module2.sh --check
• Next: Next module in course
learn_verilog_systemverilog / Module 2